# ICE VTX Racing Trike

## Starting at $4279

## Super charged with technical expertise and specialist knowledge, the ICE VTX is a brand new breed of recumbent trike. ICE VTX and VTX+ trikes are built on an optimised ICE frame featuring our No Brake Steer and Rider Positioning System.

Haut du formulaire

| Chain Guard Options For ICE VTX Racing Trike |
| --- |
|  | ICE Chain Ring Guard Designed for the ICE standard models this optional chain ring guard is a light weight and durable unit made from heat treated Al Alloy. The guard is an added safety feature but is also very good in preventing you from accidentally brushing against the oily chain rings and avoiding the recumbent rider tell tale prints on your legs or trousers. |

| Boom Easy Adjust Options For ICE VTX Racing Trike |
| --- |
|  | ICE Easy Adjust Chain Kit w/o Chain Guard The easy adjust chain kit fits to the ICE and makes quick changes to the front boom length very simple. Ideal for shared use of the trike with riders of different leg length. The kit comes with quick release levers for the front boom. Easy fitting with no need to remove the chain set. Chain tubes will need to be shortened and more chain will be needed if retro fitting. |

| Cranksets Options For ICE VTX Racing Trike |
| --- |
|  | Truvativ Elita 30/39/50 170mm Triple Crank Takeoff parts from 2014 ICE VTX. |
|  | SRAM Force 22 Exogram GXP Crankset w/Bottom Bracket |

| Chain Guard Options For ICE VTX Racing Trike |
| --- |
|  | ICE Chain Ring Guard Designed for the ICE standard models this optional chain ring guard is a light weight and durable unit made from heat treated Al Alloy. The guard is an added safety feature but is also very good in preventing you from accidentally brushing against the oily chain rings and avoiding the recumbent rider tell tale prints on your legs or trousers. |

| Front Derailleur Options For ICE VTX Racing Trike |
| --- |
|  | Microshift Front Derailleur This is the standard front derailleur used by most trike manufacturers now. |
|  | SRAM Force 10-Speed 31.8mm Front Derailleur Force model has forged and anodized swing arm. Compatible with Road Double crankset like Force or Red. |
|  | SRAM Rival 31.8mm Front Derailleur Rival model has stainless steel hardware. Cast aluminum swing arm. |

| Shifters Options For ICE VTX Racing Trike |
| --- |
|  | SRAM TT500 Bar End Shifter Set The SRAM 500 Aero shift levers deliver all the features and performance of the SRAM carbon 900 Aero shifter at a lower price. The 500s also include a three position stop - an internal adjustment coin can be flipped and rotated for precise cable release tuning. |

| Rear Cassette Options For ICE VTX Racing Trike |
| --- |
|  | SRAM PG-1070 10 speed 11-36 Cassette The new 1070 cassette offers an innovative approach to 10 speed cassette design. Our Cassettes performance is optimized by tooth profile and shift ramp design for quick and positive index shifting. The cassette shifts efficiently and positively in all high performance situations. Our new cogset features a semi-spidered construction for a maximum stiffness to weight ratio and is available in seven optimized configurations to best match a wide variety of uses. |

| Rear Derailleur Options For ICE VTX Racing Trike |
| --- |
|  | SRAM X9 Type 2 Long Cage Rear Derailleur One-way roller clutch eliminates derailleur bounce and chain slap. Maintenance free design pivots on needle bearings. Cage Lock makes wheel changes much easier. Aluminum inner and outer parallelogram links. Carbon composite and aluminum pulley cage. Sealed bushing pulleys. Compatible with all SRAM 10-speed shifters. |

| Front Tires Options For ICE VTX Racing Trike |
| --- |
|  | Schwalbe Durano 20x1.1 28-406 HS399 Wire Bead Tire For mile eaters. Durano is the right choice for high mileage purposes, because no other racing tire lasts longer. |
|  | Schwalbe Kojak 20x1.35 HS385 Folding Tire Need to go fast? Really fast? The Kojak tire is light, smooth, and ready to burn up the track. This is a light weight no frills racing tire. |
|  | Schwalbe Durano Plus 20x1.1 HS399 Folding Bead Tire Maximum puncture protection for race machines! The Durano Plus has a SmartGuard belt for extremely effective protection against penetration punctures. |

| Rear Tire Options For ICE VTX Racing Trike |
| --- |
|  | Schwalbe Durano 700c For mile eaters. Durano is the right choice for high mileage purposes, because no other racing tire lasts longer. |
|  | Schwalbe Durano Plus 700 x 23C(23-622) HS399 Folding Tire Maximum puncture protection for race machines! The Durano Plus has a SmartGuard belt for extremely effective protection against penetration punctures. |
|  | Schwalbe Ultremo ZX - 700x23C Folding Tire Schwalbe: As tire designers the Ultremo is the pinnacle of our ambition. We strived relentlessly to increase its speed and installed the ZX with HD Speed Guard and RaceStar Triple Compound. Both components are perfectly tuned to the requirements of an outstanding competition tire. |

| Fenders Options For ICE VTX Racing Trike |
| --- |
|  | ICE 700 Rear Mudguard |
|  | ICE Front Fender Mudguards These ICE Mudguards are quickly fitted and removed with one bolt (or optional QR levers). Light weight and adjustable for larger tire clearance up to 2" (50mm) Schwalbe Big Apple. Complete with mud flap at the lower edge. Comes as a set of two front Mudguards (fenders) for your Trice recumbent ICE Trike. |
|  | ICE Front 20in and Rear 700 Mudguard Fender Set |

Chain Options For ICE VTX Racing Trike

YBN 10SC 10-Speed Chain Takeoff parts from 2014 ICE VTX.

| Idler Options For ICE VTX Racing Trike |
| --- |
|  | ICE Speed-Tech Idler Pully |

| Return Idler Options For ICE VTX Racing Trike |
| --- |
|  | ICE Custom Low Friction Chain Tube |

| Front Brakes Options For ICE VTX Racing Trike |
| --- |
|  | Avid BB7 160mm Disc Brakes This kit includes everything you need to upgrade your trike's brake system to the best mechanical disc brake system available. Perfect for for any homebuilds. |
|  | Tektro Hydraulic Brakes |

| Brake Levers Options For ICE VTX Racing Trike |
| --- |
|  | Avid Speed Dial 7 Levers The Speed Dial 7 brake levers allow you to change the pull leverage to get the perfect braking feel. The levers will work with all of our mechanical brakes (Unique and Avid). We highly recommend these for use with the Avid BB7s. |

| Rear Brake Options For ICE VTX Racing Trike |
| --- |
|  | Avid BB7 Rear Disc Parking Brake Upgrade Kit - Friction Lever Complete kit to allow the addition of a rear parking brake. Includes an Avid BB7 mechanical disc brake and rotor, parking brake lever for fitting on the handle bar and a cable. The rear hub must be disc brake compatible and ready to take the rotor supplied in the kit. |

| Seat Options For ICE VTX Racing Trike |
| --- |
|  | ICE Air-Pro GRP Hardshell Seat (Large) |
|  | ICE Air-Pro GRP Hardshell Seat (Medium) |
|  | ICE Air-Pro Carbon Seat (Medium) |
|  | ICE Air-Pro Carbon Seat (Large) |

| Mirror Options For ICE VTX Racing Trike |
| --- |
|  | Zefal Spin Mirror Retractable handle-bar-end-mirror. The Zefal Spin is a small and sleek mirror option for those that want a minimalist look. Ideal for mounting on the lower portion of the handlebar with the ICE mirror mounts. |
|  | Double Zefal Spin Mirrors |

| Mirror Mounts Options For ICE VTX Racing Trike |
| --- |
|  | ICE Mirror Mount The ICE Mirror Mount attaches just below the hand grip providing you with an alternative fixing point for your mirror. (Mirror not included). Works with other trikes too. Provides a 7/8in tube to mount shifters, computers, lights and more. |
|  | Double ICE Mirror Mounts |

| Headrest Options For ICE VTX Racing Trike |
| --- |
|  | ICE Adjustable Neck Rest - For Hardshell Seat Fully adjustable for height and angle, removable padded cover. Very comfortable going up hills especially when the trike is set to a more reclined seat angle. Also a nice feature when relaxing at a standstill. |

| Flag Options For ICE VTX Racing Trike |
| --- |
|  | ICE 3 Piece Reflective Flag |

| Water Bottle Holder Options For ICE VTX Racing Trike |
| --- |
|  | ICE Bottle Cage Riser The bottle cage riser is custom built by ICE to ensure easy access to your water bottle. The bottle riser mount fits directly in-front of the rider and raises the angle of the bottle cage allowing the cage to be fitted facing the rider. This means that the bottle can be extracted in the laid back position and by pulling towards the rider. Some bottle cages wont work in conjunction with the ICE Bottle Cage Riser.(Bottle cage not included) |

| Cargo Bag Options For ICE VTX Racing Trike |
| --- |
|  | Radical Radical Allfa Side Pannier S 2x20L (pair/neck rest required) |
|  | Radical Banana Racer Bags 2x12.5L for Air Pro Seats |

| Rear Cargo Rack Options For ICE VTX Racing Trike |
| --- |
|  | ICE Rear Rack with Hardware for 26/700 rear The ICE rear rack complete with custom fixing kit is the ideal complement to your ICE trike giving a robust luggage carrying system. Maximum rack load - 25kg (55lbs |

| Computers and GPS Options For ICE VTX Racing Trike |
| --- |
|  | Cateye Strada Wireless Cycle Computer The Strada Series redefines cycle computer design with slim sizes, larger screens and font sizes with tons of functions. Our most popular computer. |
|  | Cateye Stealth10 CC-GL10 GPS Cycle Computer The Cateye Stealth10 is a GPS cyclocomputer that will store up too 60 hours of data, that can be downloaded, and reviewed on a pc. The Stealth 10 is set-up free and uses GPS technology to calculate your position quickly. Track speed, distance, elapsed time and record up to 60 hours of data that you can upload and share via web-based training sites. Monitor performance and stay motivated with online challenges. |

|  | Sigma ROX 5.0 Triple Wireless Computer w/Speed, Cadence, Heart Rate Digitally encoded 3-channel wireless STS allows riders to use several sensors, such as pulse measurement, speed and cadence transmitter, at the same time Features 64 total functions in 12 different categories |
| --- | --- |
|  | Cateye Stealth50 CC-GL50 GPS Computer ANT+ The Cateye Stealth50 gps is designed for competitive cyclists, and those want to keep track of heart rate, cadence, and power output. The Stealth50 is ANT+ compatible allowing you the same course tracking abilities as the Stealth10 but with the addition of those crucial training features, that allow you to set goals and surpass them. |
|  | Garmin Edge 810 Cycling Computer Featuring navigation and advanced training capabilities in one device, the touchscreen Edge 810 is designed for the cyclist who wants it all. |
|  | Garmin Edge 810 Cycling Computer Bundle HR/Cadence/Map Featuring navigation and advanced training capabilities in one device, the touchscreen Edge 810 is designed for the cyclist who wants it all. |

| Computer Sensor Mount Options For ICE VTX Racing Trike |
| --- |
|  | ICE computer sensor mount Used if disc brakes are fitted (not needed with the Strada Cordless with drum brakes). Attaches to the end of the kingpost arm and allows the sensor to be easily positioned to pick up the magnet signal. |

| Computer Display Mount Options For ICE VTX Racing Trike |
| --- |
|  | ICE central computer display mount To allow easy fitting of the computer head unit if the mirror fixing position is not desirable. The mount is removable and is fitted to the bottle boss mounts on the top of the main frame (a bottle cage and bottle can also be fitted at the same time) |

| Tools Options For ICE VTX Racing Trike |
| --- |
|  | Park IB-1 I-Beam Fold Up Hex Wrench/Screwdriver Set Perfect for taking on rides, the strong, compact, lightweight IB-1 |

|  | Park IB-2 I-beam Mini Fold Up Hex Wrench/Screwdriver Strong, compact and lightweight, the IB-2 is a great tool for taking on the road or trail. |
| --- | --- |
|  | Park MTB-7 Rescue Tool An outstanding value, the quality MTB-7 Rescue Tool is packed with 21 useful tools for emergency repairs on the road or trail. Includes nylon carrying case with embroidered Park Tool logo. – (More Details) |
|  | Park WTK-1 Essential Tool Kit Designed for the casual cyclist, the economical WTK-1 contains the tools needed for many basic adjustments and repairs at home or on the road/trail. |
|  | Park MTB-3.2 Rescue Tool |

|  | Park Tool BTR-1 Tool Roll Ride saving essentials in a tight tool roll, perfect for just about any rider. Nylon tool roll with cinch strap includes essential tools needed to fix a flat or roadside repairs. |
| --- | --- |
|  | Pedros Apprentice Tool Kit Portable Tool Kit Inspired by Pedro's unrivaled MTK, the new Apprentice Tool Kit offers 22 handpicked professional tools enclosed in a high quality, blow-molded hard case. |

| Pump Options For ICE VTX Racing Trike |
| --- |
|  | Topeak Mountain Morph Pump The Topeak Mountain Morph Pump is an essential ride tool. This pump produces a high volume of air, and has a foot pedal for easy tire inflation. |
|  | Topeak Road Morph Frame Pump with Gauge Topeak's Morph guage pump offers the best features of both a floor pump and a frame pump. It's small enough to carry on your bike using the included frame mount, yet offers the full inflation power of a floor pump. |

|  | Topeak Mini Morph Pump Topeak's Mini Morph pump offers the best features of both a floor pump and a frame pump. It's smaller than the original Morph pump, but big enough to achieve whatever psi your tire can handle. |
| --- | --- |
|  | Topeak RaceRocket MT Frame Pump |

| Quick Release Kit Options For ICE VTX Racing Trike |
| --- |
|  | Pair of QR levers for front boom If you would like to be able to fold your ICE trike without any tools, the ICE quick release kit for enhanced tool-less folding / split down would be perfect. |

# Schwalbe Kojak 20x1.35 HS385 Folding Tire

|  | Need to go fast? Really fast? The Kojak tire is light, smooth, and ready to burn up the track. This is a light weight no frills racing tire. Bas du formulaire |
| --- | --- |

.

### The ICE VTX Features:

Un-hinged folding frame 
Schwalbe Durano 700c rear wheel and 20" front wheels
V section white rims with red anodised nipples
Air-Pro glass fibre hard-shell seat
Avid BB7 disc brakes
SRAM X9 type 2 components
32.9lb (14.pkg) weight
Adjustable seat recline from 25 degreed upwards

2014 ICE Brochure

The Air-Pro Glass and Air-Pro Carbon are handmade composite hard-shell seats that provide exceptional stiffness with minimal weight. The Air-Pro seats are fitted as standard on the VTX and VTX+. The Air-Pro shell is anatomically shaped for comfort, supports through aggressive cornering and provides a firm brace to pedal against. Fitted to the shell is a custom composite foam cover made from breathable materials and incorporating ventilation channels, which allows air to flow across the back to aid cooling and comfort. Please see rider size guide to choose the correct seat size, note Max rider weight 230lbs (104Kg).

ICE Speed-Tech Idler Pully

Front rims - Alex DA16 Aero White 
Front hubs - ICE SL32 with sealed cartridge bearings, White
Spokes & nipples - Stainless black double butted with red alloy nipples

ICE optimised frame with 4130 Chromoly steel cruciform

ICE Custom Lightweight One-peice Handlebar.

| Detailed Specifications |
| --- |
| Frame Material | 4130 Chromoly cruciform 7005 heat treated boom and rear section |
| Trike Weight | 32.9lbs (14.9kg) |
| Total Weight Capacity | 230lbs (104kg) |
| Wheelbase | 48.03"-49.21" (1220mm-1250mm) |
| Wheel Track | 27.5" (700mm) |
| Total Length | 78.5"-88" (1994mm-2235mm) |
| Total Width | 29.5" (750mm) |
| Total Assembled Height | 26.92" (684mm) |
| Ground Clearance | 2.69" (68.5mm) |
| Bottom Bracket Height | 11.69"-15.59" (297mm-396mm) |
| X-Seam Range | 37"-48" (940-1219mm) |
| Gear Inch Range | 22.5-122.72 |
| Steering Type | Indirect |
| Steering Pivot Type | FSA Orbit-X A-head Type Headsets |
| Turning Circle | 18ft (5.5m) |
| Seat Height | 6.5" |
| Seat Angle | 25-32 degrees |
| Country of Origin | UK/Taiwan |
| Warranty | 10 year warranty for original owner with activation |

Bas du formulaire